## Slide 1: FPAW Spring 2026 Adverse Weather in Airline Operations
Captain Christian Amaral
Air Traffic Safety Group

## Slide 2: Clouds/Visibility?
What’s a go/no-go decision????
Confirmation Bias may be biggest threat!

## Slide 3: Inflight Icing?
Generally, very minor
  Jets: Greatest ice buildup on lengthy downwind in damp, cold conditions
  Props: Pick up significantly more icing in same conditions
Roselawn, IN – American Eagle ATR-72, 1994
  ATR icing limitations poorly understood
  Met knowledge/first principles might have helped!
ATS Group

## Slide 4: Density Altitude/“Hot and High” Impacts?
  Can impact payload
  Workarounds
    Thrust
      Normally “Trick” into Reduced
    Tire Speed Limits
    “Bleeds Off” Takeoff
ATS Group

## Slide 5: When Those Run Out…
DEN, Summer 2023, CRJ700 DEN-SBP
Airport elevation: 5434’
ATIS:
  F 1653Z 200/11G15 8SM HZ FEW050 33/7 3010 (Boarding time)
  G 1753Z 180/10G17 8SM HZ SKC 35/7 3011
  H 1853Z 220/9G17 7SM HZ SKC 38/8 3010
Started with 70 pax (out of 76 seats), ended with 58!
ATS Group

## Slide 6: Convective Impacts – Part 1 KBTV-KDEN – August 2025
Arrival Planned for 0000Z
Destination Weather TAF
012330Z 0200/0304 160/8 P6SM FEW 030
FM1500 21015G28 P6SM FEW035 SCT500
FM1800 24022G30 P6SM VCTS SCT035CB
FM1900 VRB25G35 TSRA SCT035CB
TEMPO 0220/0302 1/2SM +TSRA GS SCT040CB
BECMG 0301/0303 NSW SKC
ATS Group

## Slide 7: Flight Plan/Initially Cleared Route
ATS Group
TSRA

## Slide 8: Fuel Planning
Landing DEN with 12k lbs fuel (~2 hrs 20 minutes) 👍
  Alternate 1: KICT – 3.7k lbs fuel
  Alternate 2: KGJT – 3.2k lbs fuel
Fuel required: fly to destination, go missed, then proceed to most distant alternate, and land with no less than 45 minutes of fuel
This leaves ~40 minutes of hold fuel
ATS Group

## Slide 9: Enroute Considerations/Monitoring
A few shortcuts successful early
Convection blossoming all over Rockies
Still plenty of runway for daytime heating
  KGJT viable???
KICT: VFR/NSW
Not many nearby divert options clear of wx
ATS Group

## Slide 10: Somewhere west of PXV…
Reroute: After HALEN direct BUMMP.SSKII4 arrival
Adds ~400 miles
More in the path of weather
Narrows diversion options and wipes out hold fuel
Dispatch consulted, alternate changed to COS, but cells nearby and expanding
Overweight for landing in ICT
ATS Group
.

## Slide 11
What should we do?
The Slido app must be installed on every computer you’re presenting from
Do not edit How to change the design

## Slide 12: What we actually did…
Got dispatcher concurrence to land short in ICT
  Required off course vector and early descent to get below MLW
  Gassed up, and released 30 minutes later
Might have been nice to hold in between, but in the way at FL340 (ish), and descents narrow options
ATS Group

## Slide 13: Convective Impacts – Part 2 KEWR-KTPA
Arrival time TAF
  FM1600 200/09 P6SM SCT 025
  FM1800 PROB30 +TSRA
Enroute prep – TEM
Approaching Final Approach Course…
ATS Group

## Slide 14: Convective Impacts – Part 3 KDEN-KMTJ
ATS Group

## Slide 15: Turbulence?
Significant
Currently leading cause of Part 121 NTSB Classified Accidents
Data hugely important for seatbelt sign/service planning
Still astonishingly dynamic
  Operator’s weather knowledge remains crucial!!
ATS Group

## Slide 16: Conventional Turbulence PIREPS?
ATS Group
I give you…the Tempest Prognosticator
Subjective
Sparse
Stale

## Slide 17: Automatic Turbulence Reporting
Variety of products and methodologies
  Aircraft-measured vs. EFB/device based
  Outputs differ
  Despite differences, vastly superior to PIREPs alone
  BUT, frequently proprietary
ATS Group

## Slide 18: Wet/Snowy Surfaces?
Runway Condition Codes issued by FICON NOTAM
What about very dynamic conditions?
  Heavy rain
  Snow/Freezing Precip
ATS Group

## Slide 19: Winter Weather – DEN-BOS February 2026
Planned arrival 0350Z – 2 Alternates listed
KBOS TAF
FM 2100 190/10 P6SM OVC015
FM 0300 210/08 2 SM –SN
TEMPO 0305 210/8 ½ SM SN OVC 007
FM 0600 230/15 P6SM BKN 025
ATS Group

## Slide 20: Enroute Considerations
TEM
  Conservative Landing Distance Assessments for multiple runways
  Approach considerations
  Runway Turnoff
ATS Group

## Slide 21: How it Went…
BOS ATIS Q SPECI 0325Z 170/8 1SM –SN OVC009 3021
BOS ATIS R SPECI 0333Z 160/7 1/2SM SN OVC007 3020 RVR22L 3500
#3 for landing, pivot to 15R for lower mins
1 aircraft lands, runway taken for snow removal, how about 4R?
BOS ATIS S 0353Z 200/9 3/4SM SN OVC008 3018 RVR22L 5500
Rapid improvement in vis during final
Despite advertised FICON of 5/5/5, actual BA Medium (3/3/3)
”Traffic on a 2-mile final, Can you get K?”
ATS Group

## Slide 22: Impostor Syndrome??
Be not Afraid!
  Excellent equipment with high levels of redundancy
  Top-notch Training and Standardization
  OCC/Dispatch Support and resources
  Be Patient: savor time spent in the right seat
ATS Group